## Slide 1
Milwaukee Metropolitan Sewerage District
How WIMS is Used for Monitoring Renewable Energy and Energy KPIs at MMSD
Tanya Gregg, P.G.
Systems Monitoring Data Analyst
Milwaukee Metropolitan Sewerage District Special thanks to Sid Arora (MMSD)

## Slide 2
Milwaukee Metropolitan Sewerage District
MMSD Serves:
1.1 Million Customers
28 Municipalities
411 Square Miles

## Slide 3
- Water Reclamation Facilities (WRFs)
Jones Island (JI) - 1925
South Shore (SS) - 1965
  (Managed by Veolia)
- Two Inline Storage Systems
432 MG
89 MG
- 300 miles of Interceptors
from 6 to 150 inches
MMSD
Milwaukee Metropolitan Sewerage District

## Slide 4: Water Reclamation Facility Jones Island
Milwaukee Metropolitan Sewerage District
Peak flows: 330 MGD
Dry weather flows: 60-70 MGD
Mostly combined sewer area
Conventional activated sludge
Sludge drying and dewatering
Milorganite production

## Slide 5
Natural Gas to supplement LFG turbine waste heat
Electricity
Electricity for Plant Needs
Natural Gas
Landfill Gas
MMSD Energy
Combined Heat and Power System
Natural Gas (building heat)
Solar Turbine Generators 4.5 MW each – LFG/NG
Waste
heat
Jones Island WRF
Dryers
Milwaukee Metropolitan Sewerage District
Courtesy of Sid Arora, MMSD
GE Turbine Generator
15 MW – NG
Plant Electric Load 11.0 MW
Notes: JI Combined Heat and Power: turbines convert natural gas to electricity for plant use
Utilize waste heat for drying biosolids
Create Milorganite
Commercial fertilizer

## Slide 6: Water Reclamation Facility South Shore
Milwaukee Metropolitan Sewerage District
Peak flows: 300 MGD
Dry weather flows: 60-70 MGD
Separate sewer area
Conventional activated sludge, chemical P removal
12 digesters
CHP using digester gas
Notes: Digester gas engines at South Shore
  Engine generators at SS produce electricity
  Utilize waste heat
  Biosolids also pumped from JI
Still must purchase significant $ of electricity

## Slide 7
South Shore Digester Gas Production and Utilization
Anaerobic Digesters
15 MG
98oF
Feed Sludge
-Primary Sludge
-Airport Deicing Fluid
-High Strength Waste
-TWAS
Gas Storage
Spheres
Digested Sludge
Sent to Jones Island
for Milorganite Production
Gas Compressors
Flares
4 CAT Engine Generators- 0.9 MW each
White Superior Engine Generator- 1.5 MW
Digester Gas
Digester Gas/Natural Gas
Heat Recovery System
Boilers
Plant Electric Load 5.0 MW
Milwaukee Metropolitan Sewerage District
Courtesy of Sid Arora, MMSD
Electricity
Notes: Electricity to drive plant operations:
Aeration: 35%
Drying and dewatering facility: 21%
Deep tunnel pumping: 10%
Raw WW pumping, prelim, primaries: 10%
Natural gas driven turbines to generate plant electricity
Natural gas for biosolids dryers (when turbines are off) and heating
Waste heat from turbines to dry biosolids
Waste heat from engine generators for building heat and heating digesters

## Slide 8: MMSD Renewable Energy KPIs
2035 Strategic Vision (Adopted Dec. 2010):
  Meet a net 100% of energy needs with renewable energy sources
    Historical Data - good data to compare
    Metering resources of energy data
    Performance trends and reporting
  Meet 80% of energy needs with internal, renewable sources
    Sub metering to determine where needs
    Alternate fuel sources
  Reduce carbon footprint by 90% from its 2005 baseline
    Emissions data capture
    Project / scenario forecasting
Milwaukee Metropolitan Sewerage District
Notes: Historical data – ensure that all values are coming into Hach. Are

## Slide 9: Hach WIMS and MMSD Energy Monitoring
Energy Data and Hach Process:
2013 – Decision to use Hach as data management for energy data
2014 – Closer look into Energy monitoring in Hach
  New Variables, graphs, report
  Air Permit Monitoring Report
2015 - 2016 – Energy Dashboards
  New variables, unit conversions
  Energy Reports, graphs, KPIs
  Main dashboards for MMSD users
2016 - 2018
  Advanced Report Development
  New Power Meters (sub-metering)
  WE Energies Import
  Future Forecasting - > SCOPE 5
Milwaukee Metropolitan Sewerage District

## Slide 10: Hach WIMS and MMSD
Hach WIMS:
4 Facilities
  (GW, Conv, JI, SS)
Shared by Veolia
~12,800 variables
Milwaukee Metropolitan Sewerage District

## Slide 11
Milwaukee Metropolitan Sewerage District
Hach WIMs Energy Monitoring
Energy Variables
Hach Energy Data:
Location Groups
Energy Variables
  JI ~490
  SS ~260
Data Flow Processes:
Historian Collector – SCADA DATA
LIMS
Operator Entry
Notes: First Steps: Build new variables to compare historical data to and conduct QA/QC.

## Slide 12: JI Water Reclamation Facility Energy Reporting
Milwaukee Metropolitan Sewerage District
Energy Monitoring Reports:
  Air Permit Monitoring Report
    QA/QC data
    Quick indication of outliers
  LFG Monitoring
    Performance Monitoring
    Pipeline Issues
  Power Generation/Usage
    Track electricity generation and plant loads
    Quick analysis of issues
  Fuel Usage
    NG vs LFG vs WH
  Dryer – WH monitoring
    Dryers in Service
    WH Usage
  Soil moisture trigger reports
    Soil moisture related to LFG

## Slide 13: JI Water Reclamation Facility Energy Trends
Milwaukee Metropolitan Sewerage District

## Slide 14: JI Water Reclamation Facility Energy Reporting
Milwaukee Metropolitan Sewerage District

## Slide 15
Milwaukee Metropolitan Sewerage District
JI Energy Dashboard
Notes: Started in 2015 with a whiteboard and an idea. Developed new variables to get consistent units, new graphs, and reporting tools.

## Slide 16: Water Reclamation Facility Energy KPIs at Jones Island
Milwaukee Metropolitan Sewerage District

## Slide 18: South Shore WRF Fuel & Electricity
Milwaukee Metropolitan Sewerage District

## Slide 19
Milwaukee Metropolitan Sewerage District
South Shore WRF Engines Maintenance

## Slide 20: Water Reclamation Facility Energy KPIs at South Shore
Milwaukee Metropolitan Sewerage District

## Slide 21: Hach WIMS and MMSD Energy Monitoring Next Steps
Energy Data and Hach Process:
2018 & Beyond
  Future Forecasting - > SCOPE 5 & other applications
  Individual process unit KPI development
  Identify projects/processes for cost and energy savings
  Identify Energy reduction considerations
Hach WIMS:
2018 & Beyond
  WE Energies Import
  Vehicle fuel consumption import
  Hach Trends / Reporting for long-term
  KPI Report development
Milwaukee Metropolitan Sewerage District

## Slide 22: Thank you! Questions???
Milwaukee Metropolitan Sewerage District